## Slide 1: Migrating models from other solvers to use the Gurobi solver
Thank you for joining us. We’ll be starting shortly.

## Slide 2: Migrating models from other solvers to use the Gurobi solver
Renan Garcia, Ph.D., Gurobi Optimization
David Nehme, Ph.D., Abremod

## Slide 3: Renan Garcia, Ph.D.
Optimization Support Engineer at Gurobi Optimization
Ph.D. in Industrial and Systems Engineering, Georgia Tech
Expert in optimization modeling and software development
Over a decade of experience implementing decision support systems

## Slide 4: David Nehme, Ph.D.
Todo: add David's bio, change pic?

## Slide 5: Agenda
Switching is easier than you may think
Common migration scenarios
Migrating from OPL
Migration library for CPLEX Concert API
Best practices, limitations and considerations

## Slide 6
Switching is Easier Than You May Think

## Slide 7: Key Migration Issues
Building the model
  How do I build my optimization model?
  Do I build it one constraint at a time, or do I build an entire constraint matrix?
Setting solver parameters
  What solver parameters do I change?
  What effects are these changes intended to produce?
Computing and extracting the solution
  How do I extract the solution produced by the solver?
  Am I looking for an optimal solution, or just a good feasible solution?

## Slide 8: Interfacing with Gurobi
Command-Line Tool
Full-featured Interactive Shell
Matrix-oriented APIs
  C, MATLAB, R
Object-oriented APIs
  C++, Java, .NET, Python
Modeling systems
  Commercial: AIMMS, AMPL, Frontline Solvers, GAMS, MPL, …
  Free: CMPL, JuliaOpt, OSI, PuLP, PYOMO, SolverStudio, YALMIP, …
Other languages possible, but not officially supported

## Slide 9: Do-It-Yourself Resources on gurobi.com
Switching guidance: https://www.gurobi.com/resources/switching-to-gurobi/switching-overview
Documentation: https://www.gurobi.com/documentation/
  Quick Start Guides
  Reference Manual
    APIs
    Attributes
    Parameters
    Tuning
    …
  Example Tour
    22 functional examples
Seminars and videos: https://www.gurobi.com/resources/seminars-and-videos/seminars-videos

## Slide 10
Common Migration Scenarios

## Slide 11: Scenario 1: Migrating with Model Files
Example: performance testing
Export model file with virtually no changes needed to existing code
  Gurobi supports several file formats (MPS, LP, …)
Export guidance: https://www.gurobi.com/resources/switching-to-gurobi/exporting-mps-files-from-competing-solvers
Use Gurobi Command-Line Tool to solve the model
  Usage: gurobi_cl [parameters] filename
  Ex: gurobi_cl TimeLimit=3600 misc07.mps
"Quick-and-dirty" approach
  Limited ability to interact with solver (parameters only)
  For more control, try Gurobi Interactive Shell

## Slide 12: Gurobi Parameters
Control algorithmic behavior
  Defaults validated against large internal test set of models
Termination criteria
  Ex. TimeLimit, SolutionLimit
Tolerances
  Ex. MIPGap, BarConvTol
Simplex and barrier
  Ex. Method, Crossover
MIP and MIP cuts
  Ex. MIPFocus, ImproveStartTime
MIP cuts
  Ex. Cuts, GomoryPasses
Tuning and distributed algorithms
  Ex. TuneJobs, WorkerPool
General
  Ex. Presolve, OutputFlag

## Slide 13: Scenario 2: Using a Modeling System
Example: model is written in AMPL
With independent modeling systems, migrating is extremely easy
  Obtain license
  Set solver to Gurobi
    Ex: in AMPL model file, add
    option solver gurobi_ampl;
  Convert parameter settings
    Ex: in AMPL model file, add
    option gurobi_options 'mipfocus 1';

## Slide 14: Gurobi Python Environment
High-level optimization modeling constructs embedded in Python programming language
  Combines expressiveness of a modeling language with the power and flexibility of a programming language
Design goals:
  Require minimal programming skills to get started
  Bring "feel" of a modeling language to the Python interface
  Allow for code that is easy to write and maintain
  Maintain unified design across all of our interfaces
  Remain lightweight and efficient (memory & CPU) when compared with solver alone
  Support all solver and programming needs
Several videos on this topic at https://www.gurobi.com

## Slide 15: Interactive Examples

## Slide 16: Scenario 3: Porting Matrix-Oriented Code
Example: C program which uses CPLEX Callable Library, XPRESS, …
Gurobi's C API supports sparse matrix format
  Standard format used by many solvers
    Simple arrays represent matrix coefficients and their index positions
  Ex: GRBaddconstrs(), GRBaddvars()
  Virtually no changes required to existing code
Gurobi also supports advanced features
  Callbacks
  Advanced simplex routines (querying tableau rows)
  …
Must consider some Gurobi-specific modeling features when porting existing code
  Gurobi environments
  Lazy updates
  Attributes

## Slide 17: Gurobi Environments
Models are built from an environment
Parameters are set on an environment
Models get their own copy of the environment
  Once a model is created, subsequent parameter changes in parent environment are not reflected in model environment
  Use getEnv() functions to get the environment from model
Setting parameters in C
  Ex: set time limit of 3600 seconds for parent environment
  status = GRBsetdblparam(env, "TimeLimit", 3600);
  Ex: set presolve level to 2 for model's environment
  status = GRBsetintparam(GRBgetenv(model), "Presolve", 2);

## Slide 18: Lazy Updates
Gurobi updates models in batch mode
  Model creation and updates are efficient
Must call GRBmodelupdate() function to use model elements
  Ex: Call after creating a variable before using it in a constraint
  May require changes to code for other solvers
UpdateMode=1 parameter setting allows you to use elements immediately

## Slide 19: Attributes
Unified system to access model elements
  Attributes work the same across all Gurobi interfaces
Attributes refer to model elements
  Access via a basic set of get and set functions
    Attribute name is specified as a parameter
  Replaces many functions used by other solvers
Getting/Setting attributes in C
  Use get/set functions by type (int, double, char, string)
  Ex: query number of nonzeros in a model
  status = GRBgetintattr(model, "NumNZs", &nzs);
  Ex: query solution vector
  double x[NUMVARS];
  status = GRBgetdblattrarray(model, "X", 0, NUMVARS, x);
  Ex: modify constraint RHS to 1
  status = GRBsetdblattrelement(model, "UB", cidx, 1.0);

## Slide 20: Scenario 4: Porting Object-Oriented Code
Example: Java program which uses CPLEX Concert Technology
Gurobi's OO APIs represent models using objects
  Objects for variables and constraints
  Methods are used to create model elements
  Ex: add simple constraint x+y≥1 in C++
  c1 = model.addConstr(x + y >= 1, "c1");
All Gurobi APIs are just thin layers on top of same native C code
Must consider same Gurobi-specific modeling features when porting
  Subsequent parameter changes in parent environment not reflected in model environment
    Java Ex: model.getEnv().set(GRB.IntParam.Presolve, 2);
  Must call model's update() method to use elements (unless UpdateMode=1)
  Use get/set methods on objects to access attributes
    Python Ex: constr.setAttr('RHS', 1.0)

## Slide 21: Solver-specific Guidance

## Slide 22
Migrating from OPL

## Slide 23
Migration Library for CPLEX Concert API

## Slide 24
Best Practices, Limitations and Considerations

## Slide 25: Questions
Please use the Question box to ask questions to the speaker